## Slide 1: Huawei OceanStor 100D Distributed Storage Architecture and Technical Principles
Department:
Prepared By:
Date: Feb., 2020
Security Level: Internal only

## Slide 2
About This Document
Overview
  This document introduces Huawei's new-gen intelligent distributed storage of OceanStor 100D (originally referred to as FusionStorage) in terms of architecture design concepts, key technical principles, and technical competitiveness.
  This document covers some capabilities listed on the roadmap. For project development, you also need to refer to the corresponding Technical Specifications List.
Intended audience
  Huawei data storage sales engineers, frontline product managers, marketing personnel, and those from peripheral domains of R&D.
Objective
  To have a deep understanding of OceanStor 100D's design concepts, key technical principles, and technical competitiveness, which helps build an expert image during customer communication
Version and date
  V1.0, 2020-02-10
Hide this page before use.

## Slide 3
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
OceanStor 100D
Block+File+Object+HDFS
Ultimate Usability
Ultimate Reliability
Ecosystem
Scenario and Ecosystem

## Slide 4
Typical Application Scenarios of Distributed Storage
Virtual storage pool
BSS
OSS
MSS
Cloud storage resource pool
VM
Storage-compute separation, implementing elastic compute and storage scaling
EC technology, achieving higher utilization than the traditional Hadoop three-copy technology
TCO reduced by 40%+ compared with the traditional solution
HPC/Backup/Archival
HPC meets requirements for high bandwidth and intensive IOPS. Cold and hot data can be stored together.
Backup and archival, on-demand purchase, and elastic expansion
Server-storage convergence, reducing TCO by 40%+
Traditional compute-storage convergence
Ethernet
Data node +
Compute node
Data node +
Compute node
Data node +
Compute node
Data node +
Compute node
Data node +
Compute node
Data node +
Compute node
Compute node
Ethernet
Compute node
Compute node
Data node
Data node
Data node
Cloud storage resource pool
Storage-compute separation
HDFS
Storage space pooling and on-demand expansion, reducing initial investment
Ultra-large VM deployment
Zero data migration and simple O&M
VM
...VM
Backup/Archive software
Cloud storage resource pool
Public cloud
File storage
VM
Application
Database service
HPC production storage
HPC backup storage
Storage archival
Tiered storage of cold data
Public and private cloud
Tiered storage from file to object service
SSD to HDD tiering
Tiered data migration/backup to the cloud
HPC full data lifecycle management
UHD
Tiering to UHD storage
Hot data
Warm data
Cold data
HDFS
Cloud service
One storage system for HPC data lifecycle management

## Slide 5: Core Requirements for Storage Systems
High scalability
Hotspot performance
Cost
Usability
I/O performance
Reliability
Data security
Features
60.7%
60.1%
58.2%
56.6%
51.5%
50.8%
47.3%
36.4%
Source: 130 questionnaires and 50 bidding documents from carriers, governments, finance sectors, and large enterprises
Distributed Storage Hot Issue Statistics
Users'
core requirements
Reliability
Scalability
Performance
Usability
Cost

## Slide 6: Current Distributed Storage Architecture Constraints
Mainstream open-source software in the industry
User LUN/File
Obj
Obj
Obj
Obj
Obj
Obj
Obj
Obj
Obj
Obj
Obj
Obj
PG
PG
PG
PG
PG
PG
PG
PG
PG
PG
PG
PG
PG
PG
PG
CRUSH map
OSD
OSD
OSD
OSD
PG
PG
PG
PG
PG
obj
File
Disk
ID
Binary Data
Metadata
Local storage
Three steps to query the mapping: LUNs or files are mapped to multiple continuous objects on the local OSD.
Protection groups (PGs) have a great impact on system performance and layout balancing. They need to be dynamically split and adjusted based on the storage scale. This adjustment affects system stability.
The minimum management granularity is by object. The size of an object is adjustable, which affects metadata management, space consumption, performance, and even read/write stability.
Mainstream commercial software in the industry
Performance | The CRUSH algorithm is simple, but does not support RDMA, and the performance for small I/Os and EC is poor. | Multiple disks form a disk group (DG). One DG is configured with one SSD cache. Heavy I/O loads will trigger cache writeback, greatly deteriorating performance.
Reliability | Design-based CRUSH algorithm constraints: uneven data distribution, uneven disk space usage, and insufficient subhealth processing | Data reconstruction in fault scenarios has a great impact on performance.
Scalability | Restricted by the CRUSH algorithm, adding nodes costs high, and large-scale capacity expansion is difficult. | Poor scalability: Only up to 64 nodes are supported.
Usability | Lack of cluster management and maintenance interfaces with poor usability | Inherit the vCenter management system with high usability.
Cost | Community product with low cost: EC is not used for commercial, and deduplication and compression are not supported | High cost: All SSDs support intra-DG deduplication and non-global deduplication, but do not support compression. EC supports only 3+1 or 4+2.

## Slide 7
Overall Architecture of Distributed Storage (Four-in-One)
Architecture advantages
Convergence of the block, object, NAS, and HDFS services, implementing data flow and service interworking
Introducing advantages of the professional storage to achieve optimal convergence of performance, reliability, usability, cost, and scalability
Convergence of software and hardware, optimizing performance and reliability based on customized hardware
O&M Plane
Cluster Management
DeviceManger
QoS
License/Alarm/
Log
Authentication
eService
Persistence Layer
Mirror Erasure Coding Fast Reconstruction Write-back Cache SmartCache
Index Layer
Write Ahead Log Snapshot Compression Deduplication Garbage Collection
VBS (SCSI/iSCSI)
Block
LUN Volume
L1 Cache
NFS/SMB
File
DriectIO L1 Cache MDS
Object
LS OSC Billing
S3/SWIFT
HDFS
Disaster Recovery
HyperReplication
HyperMetro
HDFS
NameNode
Hardware
x86 Kunpeng

## Slide 8
OceanStor 100D
Block+File+Object+HDFS
Ecosystem
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
Ultimate Usability
Ultimate Reliability
Scenario and Ecosystem

## Slide 9
Data Routing, Twice Data Dispersion, and Load Balancing Among Storage Nodes
User Data
N1
N2
N3
N4
N5
N6
N7
...
DHT loop
SLICE
vnode
vnode
vnode
vnode
Plog 1
...
Node-1
Node-0
Node-2
Node-3
Plog 2
Plog 3
Node
Basic Concepts
Node: physical node, that is, a storage server
Vnode: logical processing unit. Each physical node is divided into four logical processing units. When a physical node becomes faulty, services processed by the four vnodes on the faulty node can be taken over by the other four physical nodes in the cluster. In this case, service takeover efficiency and load balancing can be improved.
Partition: A fixed number of partitions are created in the storage resource pool. Partitions are also units for capacity expansion, data migration, and data reconstruction.
Plog: partition log for data storage, providing the read/write interface for Append Write Only services. The size of a Plog is not fixed. It can be 4 MB or 32 MB, and the maximum size is 4 GB. The Plog size, redundancy policy, and partition where data is stored will be specified during service creation. When creating a Plog, select a partition based on load balancing and capacity balancing.
Node
Front-end NIC
SSD/HDD
Partition 01
Partition 02
Partition 03
Front-end module for data dispersion
(first)
Data processing module
Data storage module for data dispersion
(second)

## Slide 10
Node-6
Node-5
Node-4
Node-3
Node-2
The I/O channels are divided into two phases:
Host I/O processing (① red line): After receiving data, the storage system stores one copy in RAM cache and three copies in SSD WAL cache of three storage nodes. After the copies are successfully stored, a success response is returned to the upper-layer application host. The host I/O processing is complete.
Background I/O processing (② blue line): When data in the RAM cache reaches a certain amount, the system calculates large data blocks using EC and stores generated data fragments onto HHDs. (③ Before data is stored onto HDDs, the system determines whether to send data blocks to the SSD cache based on the data block size.)
Node-1
RAM cache
HDD
Erasure Coding
Data
Parity
I/O Stack Processing Framework
SSD cache
SSD WAL cache
①
②
③

## Slide 11
EC: erasure coding, a data protection mechanism. It implements data redundancy protection by calculating parity fragments. Compared with the multi-copy mechanism, EC has higher storage utilization and significantly reduces costs.
EC redundancy level: N+M = 24 (M = 2 or 4), N+M = 23 (M = 3)
Partition No. | Mem1 | Mem2 | Mem3 | Mem4 | mem5 | mem6
Partition1 | node1 Disk1 | node1 Disk3 | node2 Disk7 | node2 Disk4 | node3 Disk6 | Node3 Disk4
Partition2 | node1 Disk10 | Node3 Disk11 | node1 Disk1 | node3 Disk5 | node2 Disk3 | Node2 Disk2
... |  |  |  |  |  | 
Partition | node3 Disk10 | node2 Disk11 | node1 Disk1 | node3 Disk5 | node1 Disk3 | Node2 Disk2
Node 1
Node 2
Node 3
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
EC 4+2 Partition Table
Basic principles:
When a storage pool is created using disks on multiple nodes, a partition table will be generated. The number of rows in the partition table is 51200 x 3/(N+M), and the number of columns is (N+M). All disks are filled in the partition table as elements based on the reliability and partition balancing principles.
The mapping between partitions and disks is N:M. That is, a disk may belong to multiple partitions, and a partition may have multiple disks.
Partition balancing principle: Number of times that each disk appears in the partition = Number of times that each disk appears in memory
Reliability balancing principle: For node-level security, the number of disks on the same node in a partition cannot exceed the value of M in EC N+M.
Storage Resource Pool Principles and Elastic EC

## Slide 12
EC Expansion Balances Costs and Reliability
When adding nodes to the storage system, the customer can determine whether to expand the EC. Using EC expansion can increase the number of data blocks (M) and improve the space utilization, with the number of parity blocks (M) and reliability unchanged.
...
Data blocks (22)
Parity blocks (2)
Data blocks (2)
Parity blocks (2)
EC 2+2
EC 22+2
Ascending
As the number of nodes increases during capacity expansion, the number of data blocks (the value of N in EC) automatically increases, with the reliability unchanged and space utilization improved.
EC (N+2) |  | EC (N+3) |  | EC (N+4) | 
Redundancy Ratio | Space Utilization | Redundancy Ratio | Space Utilization | Redundancy Ratio | Space Utilization
2+2 | 50.00% | 6+3 | 66.66% | 6+4 | 60.00%
4+2 | 66.66% | 8+3 | 72.72% | 8+4 | 66.66%
6+2 | 75.00% | 10+3 | 76.92% | 10+4 | 71.43%
8+2 | 80.00% | 12+3 | 80.00% | 12+4 | 75.00%
10+2 | 83.33% | 14+3 | 82.35% | 14+4 | 77.78%
12+2 | 85.71% | 16+3 | 84.21% | 16+4 | 80.00%
14+2 | 87.50% | 18+3 | 85.71% | 18+4 | 81.82%
16+2 | 88.88% | 20+3 | 86.90% | 20+4 | 83.33%
18+2 | 90.00% |  |  |  | 
20+2 | 90.91% |  |  |  | 
22+2 | 91.67% |  |  |  | 

## Slide 13
If a fault occurs, using EC reduction to write data can ensure the data write reliability. Assume that the original EC scheme is 4+2, when a fault occurs, the data will be written to the storage system in EC 2+2 mode.
EC never degrades write operation, providing higher reliability.
Process (EDS)
Disk1
Disk2
Data
Data Write in EC 4+2
EC encoding
Disk3
Disk4
Disk5
Disk6
Original data
Parity data
2+2
2+2
EC Reduction and Read Degradation Optimize Reliability and Performance
Process
(EDS)
Disk1
Disk2
Data
Data Read in EC 4+2
EC decoding
Disk 3
Disk 4
Disk 5
Disk 6
Original data
Parity data
The EC can reconstruct valid data and return the data only after read degradation and verification decoding are performed.
The reliability of data stored in EC mode decreases if a node becomes faulty. The reliability needs to be recovered through data reconstruction.

## Slide 14
High-Ratio EC Aggregates Small Data Blocks and ROW Balances Costs and Performance
Intelligent stripe aggregation algorithm + log appending: Reduces latency and achieves a high ratio of EC 22+2
Host write I/Os are aggregated into full EC stripes based on the write-ahead log (WAL) mechanism for system reliability.
The load-based intelligent EC algorithm writes data to SSDs in full stripes, reducing write amplification and ensuring the host write latency less than 500 μs.
The mirror relationship is created between the data in the Hash memory table and that in SSD media logs. After data is aggregated, random write is changed to 100% sequential write which writes data to back-end media, improving random write efficiency.
Linear space
Data Write
A
B
C
D
E
...
A
B
C
D
E
P
Q
I/O aggregation
Full stripe
LUN 0
LUN 2
4 KB
8 KB
4 KB
...
LUN 1
4 KB
8 KB
4 KB
...
4 KB
8 KB
4 KB
...
Plog
Node-0
Node-1
Node-2
Node-3
Node-4
Data storage using Append Only Plog (ROW-based append write technology for I/O processing)

## Slide 15
Inline and Post-Process Adaptive Deduplication and Compression
OceanStor 100D supports global deduplication and compression, as well as adaptive inline and post-process deduplication. Deduplication reduces write amplification of disks before data is written to disks. Global adaptive deduplication and compression can be performed on all-flash SSDs and HDDs.
OceanStor 100D uses the opportunity table and fingerprint table mechanism. After data enters the cache, the data is broken into 8 KB data fragments. The SHA-1 algorithm is used to calculate 8 KB data fingerprints. The opportunity table is used to reduce invalid fingerprint space.
Adaptive inline and post-process deduplication: When the system resource usage reaches the threshold, inline deduplication automatically stops. Data is directly written to disks for persistent storage. When system resources are idle, post-process deduplication starts.
Before data is written to disks, the system enters the compression process. The compression is aligned in the unit of 512 bytes. The LZ4 algorithm is used and deep compression HZ9 is supported.
The fingerprint table occupies a little memory, which supports deduplication of large-capacity systems.
Opportunity
table
HASH-B
Block1
Fingerprint
table
Data with low deduplication ratios is filtered out by using the opportunity table.
Write data blocks.
Direct data in the fingerprint table after post-process deduplication.
If inline deduplication fails or is skipped, post-process deduplication is enabled and data block fingerprints enter the opportunity table.
Promote the opportunity table to a fingerprint table.
Block 2
Block 3
Block 4
Block 5
Block B
Block 1
Block 2
Block 3
HASH-B
HASH-C
HASH-A
Block A
Direct data in the fingerprint table after inline deduplication.
2
1
3
5
4
Media Type | Service Type | Deduplication and Compression | Impact on Performance
All-flash SSDs | Bandwidth-intensive services | Deduplication and compression enabled | Reduced by 30%
 | IOPS-intensive services | Deduplication and compression enabled | Reduced by 15%
 | Bandwidth-intensive services | Compression enabled only | Pure write increased by 50% and pure read increased by 70%
 | IOPS-intensive services | Compression enabled only | Reduced by 10%
HDDs | Bandwidth-intensive services | Compression enabled only | Pure write increased by 50% and pure read increased by 70%
 | IOPS-intensive services | Compression enabled only | None

## Slide 16
Node 0
Node 1
Deduplication
Deduplication
Data service
Data service
Opportunity table
Fingerprint
data table
Opportunity table
Fingerprint
data table
Address mapping table
Address
mapping
table
1. Preparation
2. Injection
3. Analysis
4. Raw data read
5. Promotion
6. Remapping
7. Garbage collection
Post-Process Deduplication

## Slide 17
EDS process on Node 0
EDS process on Node 1
Opportunity table
Fingerprint
data table
Address mapping table
FPCache
1. DSC cache destage
3. Writing fingerprint instead of data
2. Looking up fingerprint for inline deduplication
Returned result
Inline Deduplication Process
Deduplication
Opportunity table
Fingerprint
data table
Deduplication
Data service
Data service
Address
mapping
table

## Slide 18
Compression Process
512 bytes
1.5 KB
2.5 KB
B3
B4
B1
B5
B2
3.5 KB
4.5 KB
5 KB
512 bytes
1.5 KB
2.5 KB
B1
B2
B3
B5
B4
3 KB
2. Compression
Data of the same size
Data after compression
Typical data layout
in storage
OceanStor 100D data layout
Compression header, which describes the start and length of compressed data
512 bytes aligned, wasting a lot of space
Waste space
I/O data
1. Breaking data into a fixed length
3. Data compaction
After deduplication, data begins to be compressed. After compression, the data begins to be compacted.
Data compression can be enabled or disabled as required based on the LUN/FS granularity.
The following compression algorithms are supported: LZ4 and HZ9. HZ9 is a deep compression algorithm and its compression ratio is 20% higher than that of LZ4.
The length of the compressed data varies. Multiple data blocks less than 512 bytes can be compacted, and then stored and aligned in the storage space. If the compressed data is not in 512-byte aligned mode, zeros will be added to improve the space utilization.

## Slide 19
Ultra-Large Cluster Management and Scaling
Storage node
Disk
Disk
Disk
Storage node
Disk
Disk
Disk
Storage node
Disk
Disk
Disk
Storage node
Disk
Disk
Disk
Disk
Disk
Disk
Storage
pool
Adding disks
Adding/Reducing storage nodes
Compute node
Storage node: node/cabinet-level capacity expansion
Adding/Deleting nodes in the original storage pool and creating a storage pool for new nodes
VBS
Compute node
VBS
Compute node
VBS
Compute node: 10,240 nodes supported by TCP, 100 nodes supported by IB, and 768 nodes supported by RoCE
Compute node
VBS
Adding/Reducing compute nodes
Network switch
ZK
ZK
ZK
ZK
Storage node
Disk
Disk
Disk
ZK
Adding/Reducing ZK disks
Control
cluster
Nine nodes supported by ZK
Storage node: on-demand disk expansion
Compute
cluster

## Slide 20
…
Compute node
Block mounting scenario:
SCSI
VSC
VBS
EDS
Storage node
OSD
Provides only interfaces and forwards I/Os. The code is simplified and does not need to be upgraded.
Each node completes the upgrade within 5 seconds and services are quickly taken over. The host connection is uninterrupted, but I/Os are suspended for 5 seconds.
EDS
Storage node
OSD
iSCSI scenario:
VBS
Connect to the backup process.
Back up the TCP connection.
Restore the TCP connection.
Shared memory
Save the iSCSI connection and I/Os.
Restore the iSCSI connection and I/Os.
Host
iSCSI initiator
EDS
OSD
Before the upgrade, start the backup process and maintain the connection with the shared memory, and complete the upgrade within 5 seconds.
Single-path upgrade is supported. Host connections are not interrupted, but I/Os are suspended for 5 seconds.
All-Scenario Online Non-Disruptive Upgrade (No Impacts on Hosts)
Component-based upgrade: Components without changes are not upgraded, minimizing the upgrade duration and impact on services.
...
...
...
x

## Slide 21
Storage node
Storage node
Storage node
...
Storage node
Storage node
Storage node
...
Disk pool
32 nodes
Disk pool
Disk pool
Storage node
Storage node
Storage node
...
32 nodes
32 nodes
Storage pool 1
Storage pool 2
Disk pool
Storage node
Storage node
Storage node
...
32 nodes
Upgrade description:
A storage pool is divided into multiple disk pools. Disk pools are upgraded concurrently, greatly shortening the upgrade duration of distributed massive storage nodes.
The customer can periodically query and update versions from the FSM node based on the configured policy.
Upgrading compute nodes on a management node is supported. Compute nodes can be upgraded by running upgrade commands.
Concurrent Upgrade of Massive Storage Nodes
Block VBS
Application
NAS private client
Application
Obj S3
Application
HDFS
Application

## Slide 22
Coexistence of Multi-Generation and Multi-Platform Storage Nodes
Pacific V3
Pacific V2
Federation Cluster Network (Data)
Multi-generation storage nodes (dedicated storage nodes of three consecutive generations and general storage nodes of two consecutive generations) can exist in the same cluster but in different pools.
Storage nodes on different platforms can exist in the same cluster and pool.
Pacific V1
Coexistence of multi-generation storage nodes in the same cluster
TaiShan 200(Model 2280)
(Kunpeng series)
2288H V5
(x86 series)
Coexistence of multi-platform storage nodes in the same cluster

## Slide 23
OceanStor 100D
Block+File+Object+HDFS
Ecosystem
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
Ultimate Usability
Ultimate Reliability
Scenario and Ecosystem

## Slide 24
Front
0
1
2
3
CORE
CORE
CORE
CORE
...
4
5
Back-end
Meta Merge
Dedup
OSD
Xnet
Xnet
Replication
CORE
CORE
CORE
0
1
2
3
CORE
CORE
CORE
CORE
...
4
5
Xnet
CORE
CORE
CORE
Traditional CPU Thread Scheduling
CPU grouping is unavailable, and frequent switchover of processes among CPU cores increases the latency.
CPU scheduling by thread is in disorder, decreasing the CPU efficiency and ultimate performance.
Tasks with different priorities, such as foreground and background tasks, interruption and service tasks, conflict with each other, affecting performance stability.
Group- and Priority-based Multi-Core CPU Intelligent Scheduling
EDS
OSD
Communication thread pool
Xnet
I/O thread pool
OSD
Front
Front-end thread pool
Back-end
Back-end thread pool
Meta Merge
Metadata merge thread pool
Front
Communication thread pool
Dedup
Deduplication thread pool
Replication
Replication thread pool
EDS
I/O scheduler
Priority 1
Priority 2
Priority 4
Priority 5
Priority 1
Group 1
Group 2
Group 3
Group N
Advantages of group- and priority-based multi-core CPU intelligent scheduling:
Elastic compute power balancing efficiently adapts to complex and diversified service scenarios.
Thread pool isolation and intelligent CPU grouping reduce switchover overhead and provide stable latency.
Fast processing and return of front-end I/Os
Background I/O adaptive speed adjustment
High-performance Kunpeng multi-core CPU
CPU Multi-Core Intelligent Scheduling

## Slide 25
Multi-level distributed read cache
Multi-level distributed write cache
Various multi-level cache mechanisms and hotspot identification algorithms greatly improve performance and reduce latency in hybrid media.
Distributed Multi-Level Cache Mechanism

## Slide 26
Traditional Cross-Node EC
Intelligent aggregation EC based on append write
A1
A2
A3
A4
......
B1
B2
B3
B4
......
LUN 1
LUN 2
......
Write in place
I/O aggregation unavailable
A1
B9
A5
B5
B1
A3
B6
A8
......
A1
/
A3
/
P
Q
A1
B1
...
A2
B2
...
A3
B3
...
A4
B4
...
P
P
...
Q
Q
...
Full stripe
Node1
Node2
Node3
Node4
Node 5
Node 6
B1
/
/
/
P
Q
B6
/
/
B9
P
Q
......
Stripe1
Stripe2
Stripe3
Fixed address mapping cannot wait until data in the same stripe is written to the full stripe at the same time. As a result, the read/write amplification is 2 to 3 times of the full stripe.
A1
A2
A3
A4
......
B1
B2
B3
B4
......
LUN 1
LUN 2
......
Append Only and
I/O aggregation
A1
B9
A5
B5
B1
A3
B6
A8
......
A1
B1
A3
B6
P
Q
A1
B9
...
B1
A5
...
A3
B5
...
B6
A8
...
P
P
...
Q
Q
...
New full stripe
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
B9
A5
B5
A8
P
Q
......
New Stripe1
New
Stripe2
Intelligent cache aggregation
Irrelevant to the write address. Any data written at any time can be aggregated into full stripes without extra amplification.
Supplement read/write A2 and A4.
Supplement read/write B2, B3, and B4.
Small-block write
Performance improved by N times
Performance advantages of intelligent aggregation EC based on append write:
Full-stripe EC write can be ensured at any time, reducing read/write network amplification and read/write disk amplification by several times.
Data is aggregated at a time, reducing the CPU compute overhead and providing ultimate peak performance.
EC Intelligent Aggregation Algorithm

## Slide 27
The Append Only Plog technology provides the optimal disk flushing performance model for media.
Random Write (8 KB) |  |  | Sequential Write (8 KB Aggregation -> Large Size) |  | 
Disk Type | Performance | GC Impact | Disk Type | Performance | GC Impact
HDD | 150 IOPS / 1.2 MB/s | / | HDD | 5120 IOPS / 40 MB/s | /
SSD | 40K IOPS / 312 MB/s | Bad | SSD | 153K IOPS / 1200 MB/s | Good
SCM | 200K IOPS / 1562 MB/s | / | SCM | 640K IOPS / 5000 MB/s | /
Disks and new media have great performance differences in different I/O patterns.
Cache Linear space
A
B
C
D
......
E
A'
F
B'
A
......
A'
B
......
B'
......
Logical address overwrite
......
Plog 1
Physic address space
Plog 2
Plog 3
Data Write
Plog is a set of physical addresses that are managed based on a fixed size. The upper layer accesses the Plog by using Plog ID and offset.
Plog is append-only and cannot be overwritten.
Plog ID + offset
Plog has the following performance advantages:
Provides a medium-friendly large-block sequential write model with optimal performance.
Reduces SSD global collection pressure by sequential appending.
Provides a basis for implementing the EC intelligent aggregation algorithm.
Write new Plogs in appending mode.
Append Only Plog

## Slide 28
RoCE+AI Fabric Network Provides Ultra-Low Latency
100 Gbit/s RoCE + AI Fabric
25 Gbit/s TCP/IP 100 Gbit/s RoCE
Storage
nodes
Storage Controller
Storage Controller
Storage Controller
Storage Controller
Front-end NIC
Front-end NIC
Front-end NIC
Front-end NIC
Back-end NIC
Compute
nodes
write
read
Front-end service network
Block/NAS private client: RoCE
Standard object protocol: S3
Standard HDFS protocol: HDFS
Standard block protocol: iSCSI
Standard file protocol: NAS/SMB
Back-end storage network
Block/NAS/Object/HDFS: RoCE
AI fabric intelligent flow control: Precisely locates congested flows and implements backpressure suppression without affecting normal flows. The waterline is dynamically set to ensure the highest performance without packet loss. The switch and NIC collaborate to schedule the maximum quota for congestion prevention. The fluctuation rate of the network latency is controlled within 5% without packet loss. The latency is controlled within 30 µs.
Binding links doubles the network bandwidth.
SSD/HDD
Back-end NIC
SSD/HDD
Back-end NIC
SSD/HDD
Back-end NIC
SSD/HDD

## Slide 29
DHT algorithm
Logical space of LUN1 LBA
Grain (e.g. 8 KB)
Index Layer
Block: DHT Algorithm + EC Aggregation Ensure Balancing and Ultimate Performance
Mapping Between LBAs and Grains of LUNs | 
LUN1-LBA1 | Grain1
LUN1-LBA2 | Grain2
LUN1-LBA3 | Grain3
LUN2-LBA4 | Grain4
Mapping Between LBAs and Grains of LUNs | 
Grain1 | Four grains form an EC stripe and are stored in the partition.
Grain2 | 
Grain3 | 
Grain4 | 
Persistency Layer
DHT algorithm: (LBA/64 MB)%
I/O
Service Layer
The storage node receives I/O data and distributes the data blocks of 64 MB to the storage node using the DHT algorithm.
After receiving the data, the storage system divides the data into 8 KB data blocks of the same length, compresses the deduplicated data at the granularity of 8 KB, and aggregates the data.
The aggregated data is stored to the storage pool.
D1
D2
D3
D4
P1
P2
Partition ID
Partition ID
D1
D2
D3
D4
P1
P2
Node-2
Node-3
Node-6
Node-7
Node-5
Node-4
Node-1
Node-2
Node-3
Node-6
Node-7
Node-5
Node-4
Node-1
......
Granularity
(64 MB)
Logical space of LUN2 LBA

## Slide 30
A, AA, AB, ABA, ABB, ............, ZZZ
Node 2
Node 3
Node n
Node 1
…
Range
1. Metadata is evenly distributed in lexicographic order + range partitioning mode. Metadata is cached to SSDs.
You can locate the node where the metadata index resides based on the bucket name and prefix to quickly search for and traverse metadata.
A, AA, AB, ABA, ABB, ............, ZZZ
Range Partition
Range 1
Range 2
Range n
Range 0
...
WAL
Converged
1. The WAL mode is used. The foreground records only one write log operation for one PUT operation.
2. Data is compacted in the background.
The WAL mode reduces foreground write I/Os.
SSDs improve the access speed.
Object: Range Partitioning and WAL Submission Improve Ultimate Performance and Process Hundreds of Billions of Objects

## Slide 31
Traditional HDFS NameNode model
Only one active NameNode provides the metadata service. The active and standby NameNodes are inconsistent in real time and have a synchronization period.
If the current active NameNode becomes faulty, the new NameNode cannot provide the metadata service until the new NameNode completes the log loading. The duration is up to several hours.
The number of files supported by a single active NameNode depends on the memory of a single node. The maximum number of files supported by a single active NameNode is 100 million.
When a namespace is under heavy pressure, concurrent metadata operations consume a large number of CPU and memory resources, deteriorating performance.
Huawei HDFS Concurrent Multi-NameNode
Multiple active NameNodes provide metadata services, ensuring real-time data consistency among multiple nodes.
Avoid metadata service interruption caused by traditional HDFS NameNode switchover.
The number of files supported by multiple active NameNodes is no longer limited by the memory of a single node.
Multi-directory metadata operations are concurrently performed on multiple nodes.
HDFS: Concurrent Multiple NameNodes Improve Metadata Performance
Active
NameNode
DataNode
Active
NameNode
DataNode
Active
NameNode
DataNode
HBase/Hive/Spark
Hadoop
compute node
Hadoop
compute node
Active
NameNode
Standby
NameNode
Standby
NameNode
HA based on NFS or
Quorum Journal
HBase/Hive/Spark

## Slide 32
Key Technology | Large Files, High Bandwidth | Large Files and Random Small I/Os | Massive Small Files, High OPS | Peer Vendors
1. Private client (POSIX, MPIIO) | Multi-channel protocol 35% higher bandwidth than common NAS protocols | Intelligent protocol load balancing 45% higher IOPS than common NAS protocols | Small I/O aggregation 40% higher IOPS than common NAS protocols | Isilon and NetApp do not support this function. DDN and IBM support this function.
2. Intelligent cache | Sequential I/O pre-read improves bandwidth. | Regular stream prefetch improves the memory hit ratio and performance and reduces the latency. | I/O workload model of intelligent service learning implements cross-file pre-reading and improves the hit ratio. | Peer vendors support only sequential stream pre-reading and do not support interval stream pre-reading or cross-file pre-reading.
3. NVDIMM | Stable write latency | Stable write latency and I/O aggregation | Stable write latency and file aggregation | Only Isilon and NetApp support this function.
4. Block size of the self-adaptive application | 1 MB block size, improving read and write performance | 8 KB block size, improving read and write performance | 8 KB block size, improving read and write performance | Only Huawei supports this function.
5. Large I/O passthrough | Large I/Os are directly read from and written to the persistence layer, improving bandwidth. | / | / | Only Huawei supports this function.
Protocol
Index
Protocol
Index
Protocol
Space
Index
Persistence
Front-end network
Persistence
Persistence
Application
Private client
Back-end network
Application
Space
Space
Standard protocol client
Node 3
Read cache
Write cache
Write cache
Write cache
①
②
③
④
⑤
Private client, distributed cache, and large I/O passthrough (DIO) technologies enable a storage system to provide high bandwidth and high OPS.
NAS: E2E Performance Optimization

## Slide 33
OceanStor 100D
Block+File+Object+HDFS
Ecosystem
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
Ultimate Usability
Ultimate Reliability
Scenario and Ecosystem

## Slide 34
Based on advanced test algorithms and industry-leading full temperature cycle tests, firmware tests, ERT tests, and ORT tests, Huawei distributed storage ensures that component defects and firmware bugs can be effectively intercepted and the overall hardware failure rate is 30% lower than the industry level.
Component authentication/Preliminary test for R&D samples/Analysis on product applications
Qualification test
Failure analysis
Online quality data analysis/warning system
ERT long-term reliability test
Production test
(including temperature cycle)
ORT long-term test for product samples after delivery
Sampling test
Joint test
RMA
Reverse
Joint test
Circular improvements
(Quality/Supply/Cooperation)
Qualification test
100+ test cases:
Functions, performance, compatibility, reliability, firmware bug test, vibration, temperature cycle, disk head, disk, special specifications verification
System test
500+ test cases:
System functions and performance, compatibility with earlier versions, disk system reliability
ERT
About 1000 disks have been tested for three months by introducing multiple acceleration factors.
5-level FA analysis
I: System/disk logs
Locate simple problems quickly.
II: Protocol analysis
Locate interactive problems accurately.
III: Electrical signal analysis
Locate complex disk problems.
IV: Disk teardown for analysis
Locate physical damages of disks.
V: data restoration
Supplier
tests/audits during the supplier's production
Start:
Design review
Disk selection
Component-Level Reliability: Component Introduction and Production Improve Hardware Reliability

## Slide 35
Product-Level Reliability: Data Reconstruction Principles
Fault
Node 1
Node 2
Node 3
Node 4
Node 5
Node 6
Disk 1
Disk 2
Disk 3
Disk N
...
Disk 1
Disk 2
Disk 3
Disk N
...
Disk 1
Disk 2
Disk 3
Disk N
...
Disk 1
Disk 2
Disk 3
Disk N
...
Disk 1
Disk 2
Disk 3
Disk N
...
Disk 1
Disk 2
Disk 3
Disk N
...
Disk 4
Traditional RAID
Distributed RAID
30 minutes
5 hours
10 times faster than traditional storage
Other distributed storage
Distributed RAID
30 minutes
1 hour
Twice faster than other distributed storage

## Slide 36
HDFS
APP
Product-Level Reliability: Technical Principles of E2E Data Verification
Two verification modes:
  Real-time verification: Write requests are verified on the access point of the system (the VBS process). Host data is re-verified on the OSD process before being written to disks. Data read by the host is verified on the VBS process.
  Periodical background verification: When the service pressure of the system is low, the system automatically enables the periodical background verification and self-healing functions.
Three verification mechanisms: CRC 32 protects users' 4 KB data blocks. In addition, OceanStor 100D supports host and disk LBA logical verification to optimize all silent data scenarios, such as transition, read offset, and write offset.
Two self-healing mechanisms: local redundancy mechanism and active-active redundancy data
Block, NAS, and HDFS support E2E verification, but Object does not support this function.
EDS
OSD
SWITCH
Block
APP
HyperMetro
OceanStor 100D
①
②
③
④
⑤
512
512
512
512
512
512
512
512
4 KB Data Block
64 Bytes
Data Integrity Area
512
①WP: DIA insertion
②WP: DIA verification
③RP: DIA verification
⑤→④: Read repair from remote replication site
⑥→④: Read repair from other copy or EC check calculation
Disk
⑥
NAS
APP
S3
APP
HDFS

## Slide 37
Product-Level Reliability: Technical Principles of Subhealth Management
1. Disk sub-health management
3. Process/Service sub-health management
4. Fast-Fail (fast retry of path switching)
2. Network sub-health management
Multi-level detection: The local network of a node quickly detects exceptions such as intermittent disconnections, packet errors, and negotiated rates. In addition, nodes are intelligently selected to send detection packets in an adaptive manner to identify link latency exceptions and packet loss.
Smart diagnosis: Smart diagnosis is performed on network ports, NICs, and links based on networking models and error messages.
Level-by-level isolation and warning: Network ports, links, and nodes are isolated based on the diagnosis results and alarms are reported.
Intelligent detection and diagnosis: Information about Self Monitoring Analysis and Reporting Technology (SMART), statistical I/O latency, real-time I/O latency, and I/O errors is collected. Clustering and slow-disk detection algorithms are used to diagnose abnormal disks or RAID controller cards.
Isolation and warning: After diagnosis, the MDC is instructed to isolate involved disks and report an alarm.
NODE1
NIC
NIC
SWITCH
SWITCH
NODE2
NIC
NIC
①
②
Cross-process/service detection 1: If the I/O access latency exceeds the specified threshold, an exception is reported.
Smart diagnosis 2: OceanStor 100D diagnoses processes or services with abnormal latency using the majority voting or clustering algorithm based on the reported abnormal I/O latency of each process or service.
Isolation and warning 3: Report abnormal processes or services to the MDC for isolation and reports an alarm.
Ensure that the I/O latency of a single sub-healthy node is controllable.
I/O-level latency detection 1: checks whether the response time of each I/O exceeds the specified threshold and whether a response is returned for the I/O. If no response is returned, Fast-Fail is started.
Path switchover retry 2: For read I/Os, other copies are read or EC is used for recalculation. For write I/Os, new space is used for data write (space is allocated to other normal disks).
EDS
OSD
②
DISK
OSD
DISK
①
EDS
OSD
MDC
EDS
①
②
③
①
DISK
RAID Card
OSD
MDC
②
①
①

## Slide 38
1822 NIC
Nodes entry
process
CM
ZK
Fault notification
MDC
Fault notification
Fault notification
EulerOS works with the 1822 NIC. When a node is restarted due to the power failure, power-off by pressing the power button, hardware fault, or system reset, the 1822 iNIC proactively sends a node fault message. Other nodes quickly rectify the node fault. The I/O suspension time is less than or equal to 5 seconds.
Node entry process
Write key information in advance.
Reboot
Power-off
Unexpected power-off
System-insensitive
reset due to hardware faults
Power off the node by pressing the power button.
System reset
Power-off interruption
Reset interruption
System notification
Troubleshooting
Troubleshooting
Troubleshooting
1822 NIC
Node fault broadcast
Product-Level Reliability: Proactive Node Fault Notification and I/O Suspension for 5 Seconds

## Slide 39
Solution-Level Reliability: Gateway-Free Active-Active Design Achieves 99.9999% Reliability (Block)
OceanStor 100D A
ERP
BI
CRM
Synchronous data dual-write
SCSI/iSCSI
SCSI/iSCSI
100 KM
OceanStor 100D B
Two sets of OceanStor 100D clusters can be used to construct active-active access capabilities. If either data center is faulty, the system automatically switches to the other cluster and therefore, no data will be lost (RP0 = 0, RTO ≈ 0) and upper-layer services will not be interrupted.
The OceanStor 100D HyperMetro is based on the virtual volume mechanism. Two storage clusters are virtualized into a cross-site virtual volume. The data of the virtual volume is synchronized between the two storage clusters in real time, and the two storage clusters can process the I/O requests of the application server at the same time.
The HyperMetro has good scalability. For customers who have large-scale applications, each storage cluster can be configured with multiple nodes. Each node can share the load of data synchronization, enabling the subsequent service growth.
The HyperMetro supports the third-place arbitration mode and static priority arbitration mode. If the third-place quorum server is faulty, the system automatically switches over to the static priority arbitration mode to ensure service continuity.

## Slide 40
In normal cases, the write I/Os are written to both sites concurrently before it is returned to the hosts to ensure data consistency.
The optimistic lock mechanism is used. When the LBA locations of I/Os at the two sites do not conflict, the I/Os are written to their own locations. If the two sites write data to the same LBA address space that overlaps with each other, the data is forwarded to one of the sites for serial write operations to complete lock conflict processing, ensuring data consistency between the two sites.
If a site is faulty, the other site automatically takes over services without interrupting services. After the site is recovered, incremental data synchronization is performed.
SCSI, iSCSI, and consistency groups are supported.
Summary: With active-active mechanism, data can be consistent in real time, ensuring core service continuity.
HyperMetro member LUN
HyperMetro member LUN
HyperMetro LUN
Cross-site active-active cluster
Host
Host
OceanStor 100D A
Application cluster
Data center A
Data center B
OceanStor 100D B
5. Forwards I/O2
2. Performs dual-write for I/O1 and adds a local lock to the I/O1 range at both ends.
3. Sends I/O2.
4. Performs dual-write for I/O2. A conflict is detected based on the range lock.
6. Processes the I/O1 and then the I/O2.
1. Sends I/O1.
Key Technologies of Active-Active Consistency Assurance Design

## Slide 41
Cross-Site Bad Block Recovery
The production host reads data from storage array A.
Storage array A detects a bad block by verification.
The bad block fails to be recovered by reconstruction. (If the bad block is recovered, the following steps will not be executed.)
Storage array A detects that the HyperMetro pair is in the normal state and initiates a request to read data from storage array B.
Data is read successfully and returned to the production host.
The data of storage array B is used to recover the bad block's data.
HyperMetro LUN
Host
HyperMetro
HyperMetro member LUN
HyperMetro member LUN
1
4
5
2
Read I/O
6
3
Bad block
OceanStor 100D A
OceanStor 100D B
  The cross-site bad block recovery technology is Huawei's proprietary technology. It can be automatically executed.
Cross-Site Bad Block Recovery

## Slide 42
Remote DR center
WAN
Asynchronous replication
Production center
Asynchronous replication provides 99.999% solution-level reliability.
An asynchronous remote replication relationship is established between a primary LUN in the production center and a secondary LUN in the DR center. Then, initial synchronization is performed to copy all data from the primary LUN to the secondary LUN.
After the initial synchronization is complete, the asynchronous remote replication enters the periodic incremental synchronization phase. Based on the customized interval, the system periodically starts the synchronization task and synchronizes the incremental data written by the production host to the primary LUN from the end of the previous period to the current time to the secondary LUN.
Support for an RPO in seconds and a minimum synchronization period of 10 seconds
Support for the consistency group
Support for one-to-one and one-to-many (32)
Simple management and one-click DR drill and recovery
A single cluster supports 64,000 pairs, meeting large-scale cloud application requirements.
Solution-Level Reliability: Remote Disaster Recovery for Core Services, Second-Level RPO (Block)

## Slide 43
Load balancing in replication: Based on the preset synchronization period, the primary replication cluster periodically initiates a synchronization task and breaks it down to each working node based on the balancing policy. Each working node obtains the differential data generated at specified points in time and synchronizes the differential data to the secondary end.
When the network between the replication node at the production site and the node at the remote site is abnormal, data can be forwarded to other nodes at the production site and then to the remote site.
Asynchronous replication has little impact on system performance because no differential log is required. The LSM log (ROW) mechanism supports differences at multiple time points, saving memory space and reducing the impact on host services.
Getdelta
Getdelta
Getdelta
Getdelta
Node 1
Node 2
Node 3
Node 4
Node 1
Node 2
Node 3
Node 4
Replication cluster B
Replication cluster A
Async Replication
Summary: Second-level RPO and asynchronous replication without differential logs (ROW mechanism) are supported, helping customers recover services more quickly and efficiently.
Data Synchronization and Difference Recording Mechanisms

## Slide 44
OceanStor 100D
Block+File+Object+HDFS
Ecosystem
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
Ultimate Usability
Ultimate Reliability
Scenario and Ecosystem

## Slide 45
Install the hardware.
Install the software.
Configure the temporary network.
Install OceanStor 100D.
Scan nodes and configure the network.
Create a storage pool.
Install compute nodes in batches.
Manually install compute nodes.
Automatic node detection, one-click network configuration, and intelligent storage pool creation are supported, making services available within 2 minutes
You can install a large number of nodes in one-click mode or install them manually or by compiling scripts.
In-depth preinstallation is complete before delivery.
Out-of-the-Box Operation

## Slide 46
AI-based Forecast
eService
1. eService uses massive data to train AI algorithms online, and mature algorithms are adapted to devices.
2. AI algorithms that do not require large-data-volume training are self-learned in the device.
Disk information collection
DISK
Data input
AI Algorithms
Capacity collection
Result output
Capacity forecast
Run AI algorithms on devices based on historical capacity information to forecast risks one year in advance.
Risky disk forecast
Run AI algorithms on devices based on disk logs to forecast risks half a year in advance.
1
2

## Slide 47
Hardware-based modeling and layered display of global hardware enable second-level hardware fault locating.
Hardware Visualization
Visualized hardware

## Slide 48
Based on the network information model, collaborative network management is achieved, supporting network planning, fault impact analysis, and fault locating.
The network topology can be displayed by VLAN and service type, facilitating unified network planning.
Network visualization displays network faults, subhealth status, and performance, associates physical network ports, presents service partitions, and helps customers to identify the impact scope of faults or subhealth for efficient O&M.
Network Visualization
Visualized networks

## Slide 49
Three-Layer Intelligent O&M
Data Center
https/email
DeviceManager
Single-device management software
eSight
Storage monitoring and management
Smartkit
Storage service tool
OceanStor DJ
Storage resource control
Fault monitoring
Delivery
Resource provisioning
AAA
OceanStor 100D
Inspection
Upgrade
Scale-in/out
Deployment
Monitoring
Configuration
License management
CLI
Single-device management software
eService Cloud
Asset management
Troubleshooting
Capacity forecast
Remote monitoring
Service planning
Upgrade
Troubleshooting
Capacity forecast
Risky disk forecast
REST/SNMP/IPMI
REST/CLI
Log analysis
Inspection tool
Health evaluation
REST
Performance report
Automatic work order creation
Intelligent maintenance platform
Intelligent analysis platform
HDFS maintenance Platform
TAC/GTAC expert
R&D expert
eService
Massive maintenance data
Global knowledge base
Storage subnet topology
Correlation analysis and forecast
Cluster management
Service management

## Slide 50
OceanStor 100D
Block+File+Object+HDFS
Ecosystem
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
Ultimate Usability
Ultimate Reliability
Scenario and Ecosystem

## Slide 51
Flexible and General-Purpose Storage Nodes
TaiShan 200(Model 5280) 4 U rack storage node:
2*Kunpeng 920 CPU
36 Slot Disk
GE / 10GE / 25GE / 100 Gbit/s IB
TaiShan 200(Model 2280) 2 U rack storage node:
2*Kunpeng 920 CPU
12/25 Slot Disk or 24 Slot NVMe
GE / 10GE / 25GE / 100 Gbit/s IB
2288H V5 2 U rack storage node:
2*X86 CPU
12/25 Slot Disk or 24 Slot NVMe
GE / 10GE / 25GE / 100 Gbit/s IB
5288 V5 4 U rack storage node:
2*X86 CPU
36 Slot Disk
GE / 10GE / 25GE / 100 Gbit/s IB
Kunpeng series
x86 series
Name | Node | Node Type | Hardware Platform
OceanStor 100D | C110 | Capacity | 5288 V5
 | C100 |  | TaiShan 200 (Model 5280)
 | P110 | Performance | 2288H V5
 | P100 |  | TaiShan 200 (Model 2280)
 | F110 | Flash | 2288H V5
 | F100 | Flash | TaiShan 200 (Model 2280)

## Slide 52
High-performance all-flash
(Atlantic)
5 U, 8 nodes, 10 SSDs per node, 80 SSDs in total
Two I/O cards per node, a total of 16 I/O cards
Two switch boards, supporting eight 100GE ports and eight 25GE ports
Rear view
Front view
High-density HDD
(Pacific)
5 U, 2 nodes, 60 HDDs per node, 120 HDDs in total
Two I/O cards per node, four onboard 25GE ports
New-Generation Distributed Storage Hardware

## Slide 53
BBU
FAN
PWR
Expander
Controller
SSD
1620
1620
X15
HALFPALM
VNODE 1
Exp
X15
HALFPALM
Exp
X15
HALFPALM
Exp
X15
HALFPALM
Exp
X15
HALFPALM
Exp
X15
HALFPALM
Exp
X15
HALFPALM
Exp
X15
HALFPALM
Exp
VNODE 2
VNODE 3
VNODE 4
VNODE 5
VNODE 6
VNODE 7
VNODE 8
SAS/PCIE
SAS/PCIE
BMC
BBU
Fan module
Power supply unit
BMC
PCIe card
PCIe card
4*
25G
PCIe card
PCIe card
4*
25G
1*
GE
1*
GE
BBU
Fan module
Power supply unit
System disk
System disk
Two nodes with 120 disks provide 24 disk slots per U, with industry-leading density and the lowest TCO per disk slot in the industry.
The dual-controller switchover design of vnode eliminates data reconstruction in the case of controller failures, ensuring service continuity and high reliability.
FRU design for entire system components, independent smooth evolution for each subsystem, one entire system for ever-new data
Pacific Architecture Concept: High Disk Density, Ultimate TCO, Dual-Controller Switchover, High Reliability, Smooth Data Upgrade, and Ever-New Data

## Slide 54
Secondary controller service takeover in the case of a faulty controller
1. When a single node is faulty, SSDs are taken over by the secondary controller physically within 10 seconds, and no reconstruction is required. Compared with common hardware, the fault recovery duration is reduced from days to seconds.
2. The system software can be upgraded online and offline without service interruption.
3. Controllers and modules can be replaced online.
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
15 x HDDs
Dual-controller takeover
Single-controller SSD
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
SSD
VNODE
Controller A
Controller B
Controller A
Controller B
Enclosure 2
Enclosure 1
15 x HDDs
Single-controller SSD
Compute virtual unit
X
Vnode-level high-ratio EC N+2
1. The SSDs of a single controller are distributed to four vnodes based on the expander unit. A large-ratio EC at the vnode level is supported.
2. At least two enclosures and 16 vnodes are configured. The EC ratio can reach 30+2, which is the same as the reliability of general-purpose hardware.
3. Expansion modules (including power supplies) and disk modules can be replaced online independently.
1620
1620
X15
HALFPALM
PCIe card
VNODE 1
X15
HALFPALM
VNODE 1
X15
HALFPALM
VNODE 1
X15
HALFPALM
VNODE 1
PCIe card
4*
25G
PCIe card
PCIe card
4*
25G
SAS
X15
HALFPALM
VNODE 1
X15
HALFPALM
VNODE 1
X15
HALFPALM
VNODE 1
X15
HALFPALM
VNODE 1
SAS/PCIE
X
Vnode design supports large-scale EC and provides over 20% cost competitiveness.
If a controller is faulty, the peer controller of the vnode takes over services in seconds, ensuring service continuity and improving reliability and availability.
EC redundancy is constructed based on vnodes. Areas affected by faults can be reduced to fewer than 15 disks. A faulty expansion board can be replaced online.
Pacific VNode Design: High-Ratio EC, Low Cost, Dual-Controller Switchover, and High Reliability
Compute virtual unit
Compute virtual unit
Compute virtual unit

## Slide 55
Front view
Rear view
Flash storage native design: Fully utilize the performance and density advantages of SSDs. The performance can reach 144 Gbit/s and up to 96 SSDs are supported, ranking No.1 in the industry.
Simplified network design: The built-in 100 Gbit/s IP fabric supports switch-free Atlantic networking and hierarchical Pacific networking, simplifying network planning.
The architecture supports field replaceable unit (FRU) design for entire system components and independent smooth evolution for each subsystem, achieving one entire system for ever-new data.
Key Specifications | Requirements Specifications
System model | 5 U 8-node architecture, all-flash storage
Medium disk slot | An enclosure supports 96 x half palms.
Interface module | An enclosure supports 16 interface modules, compatible with half-height half-length standard PCI cards.
Switch | An enclosure supports two switch boards, eight controllers in the enclosure can be shared, and three enclosures can be connected without switches.
Node | A node supports one Kunpeng 920 processor, eight DIMMs, and 16 GB backup power.
CPU
......
CPU
......
......
CPU
......
CPU
......
I/O
I/O
I/O
I/O
I/O
I/O
I/O
I/O
Built-in IP Fabric
Built-in IP Fabric
Atlantic Architecture: Flash Storage Native Design with Ultimate Performance, Built-in Switch Networking, Smooth Upgrade, and Ever-New Data

## Slide 56
Traditional architecture design
1. The ratio of CPUs to flash storage is unbalanced, causing insufficient utilization of the flash storage.
2. A 2 U device can house a maximum of 25 SSDs, causing the difficulty in improving the medium density.
Atlantic architecture is designed for high-performance and high-density application scenarios.
3. The holes on the vertical backplane are small, requiring more space for CPU heat dissipation.
1. The parallel backplane design improves the backplane porosity by 50% and reduces power consumption by 15%. The compute density and performance are improved by 50%.
2. The half-palm design for SSDs reduces the thickness, increases the depth, and improves the SSD density by over 50%.
4. 2.5-inch NVMe SSDs are evolved from HDDs and are not dedicated to SSDs.
3. Optimal ratio of CPUs to SSDs: A single enclosure supports eight nodes, improving storage density and compute power by 50%.
Native all-flash design:
Matching between compute power and SSDs: Each Kunpeng processor connects to a small number of SSDs to fully utilize SSD performance and avoid CPU bottlenecks.
Native flash storage design: Flash-oriented half-palm SSD with a slot density 50% higher than that of a 2.5' disk and more efficient heat dissipation
Half PALM SSD
Native Storage Design of Atlantic Architecture

## Slide 57
4 x 100GE
4 x 100GE
4 x 100GE
64 port 100GE Switch
2 x 100GE
2 x 100GE
2 x 100GE
Switch-free design:
24-node switch-free design eliminates network bandwidth bottlenecks.
With switch-free design, switch boards are interconnected through 8 x 100GE ports.
The passthrough mode supports switch interconnection. The switch board ports support the 1:1, 1:2, or 1:4 bandwidth aggregation ratio and large-scale flat networking.
6603
6603
4 nodes, 100GE per node
4 nodes, 100GE per node
4 x 25GE
4 x 25GE
BMC
SD6603
SD6603
1620
1620
1620
1620
1620
1620
1620
1620
SD6603
SD6603
1620
1620
1620
1620
1620
1620
1620
1620
SD6603
SD6603
100GE
100GE
4*50GE
4*50GE
QSFP-DD
4*25GE
100GE
100GE
100GE
1620
1620
1620
1620
1620
1620
1620
1620
100GE
100GE
24-node switch-free networking
Large-scale cluster switch networking
Adopt the Pacific architecture to implement tiered storage.
Atlantic Network Design: Simplified Networking Without Performance Bottleneck
SD6603
SD6603
1620
1620
1620
1620
1620
1620
1620
1620
SD6603
SD6603
1620
1620
1620
1620
1620
1620
1620
1620
SD6603
SD6603
100GE
100GE
4*50GE
4*50GE
QSFP-DD
4*25GE
100GE
100GE
100GE
1620
1620
1620
1620
1620
1620
1620
1620
100GE
100GE
Atlantic
Atlantic
Atlantic
Atlantic
Atlantic
Atlantic

## Slide 58
OceanStor 100D
Block+File+Object+HDFS
Ecosystem
Ultimate Efficiency
Ultimate Performance
Overview
Hardware
Ultimate Usability
Ultimate Reliability
Scenario and Ecosystem

## Slide 59
Block Service Solution: Integration with the VMware Ecosystem
Virtualization & Cloud Management
OceanStor 100D
vCenter Plugin (storage integration management)
VASA (VVOL feature)
vROps (monitoring)
vRO/vRA (workflow)
SRM (DR)
Rest
Rest
Enhances vRO & vRA integration and supports replication, active-active, snapshot, and consistency group capabilities based on OceanStor 100D 8.0.
Interconnects with SRM to support replication, active-active switchover, switchback, and test drills and provides end-to-end solutions.
Integrates with vROps to provide O&M capabilities based on storage service performance, capacity, alarms, and topologies, implementing unified O&M management.
vCenterPlugin and VASA (Vvol) integration: provides vCenter-based integration management, enhances VVol-based QoS and storage profile capabilities, and supports VASA resource management in multiple data centers.
REST
VMware vCenter Server
VMware vCloud Director
VMware vCenter
Site Recovery Manager
VMware vRealize
Orchestrator
VMware vRealize
Operations

## Slide 60
OpenStack P release Cinder Driver API(Must Core-Function):
OpenStack P release | 
volume driver API | OceanStor 100D
create_volume | Yes
delete_volume | Yes
create_snapshot | Yes
delete_snapshot | Yes
get_volume_stats | Yes
create_volume_from_snapshot | Yes
create_clone_volume | Yes
extend_volume | Yes
copy_image_to_volume | Yes
copy_volume_to_image | Yes
attach_volume | Yes
detach_volume | Yes
initialize_connection | Yes
terminate_connection | Yes
OceanStor 100D Cinder Driver architecture:
Block Service Solution: Integration with OpenStack
Community Edition | Red Hat
OpenStack KiloOpenStack MitakaOpenStack NewtonOpenStack QueensOpenStack RockyOpenStack Stein | Red Hat OpenStack Platform 10.0
Applicable version:
Cinder API
Cinder Scheduler
Cinder Volume
OpenStack package
(OpenStack)
OpenStack plugin
(Huawei-developed)
OceanStor 100D distributed storage
OpenStack
Rest API
STaaS or eSDK

## Slide 61
CSI plugin
Deployed on all Kubernetes nodes based on the CSI specifications to complete volume creation/deletion, mapping/unmapping, and mounting/unmounting.
Management plane
Data plane
CSI plug-in assistance service provided by the Kubernetes community
Kubernetes Node
Kubernetes Master
OceanStor 100D
①
②
③
Kubernetes Node
CSI plugin
Container
/mnt
Block dev
SCSI/iSCSI
CSI plugin
driver-register
external-provisioning
external-attaching
external-attaching
CSI plugin
driver-register
driver-register
Process for Kubernetes to use the OceanStor 100D CSI plug-in to provide volumes:
The Kubernetes Master instructs the CSI plug-in to create a volume. The CSI plug-in invokes an OceanStor 100D interface to create a volume.
The Kubernetes Master instructs the CSI plug-in to map the volume to the specified node. The CSI plug-in invokes the OceanStor 100D interface to map the volume to the specified node host.
The target Kubernetes node to which the volume is mapped instructs the CSI plug-in to mount the volume. The CSI plug-in formats the volume and mounts the volume to the specified directory of the Kubernetes.
Block Service Solution: Integration with Kubernetes

## Slide 62
......
Compute Farm(50000+)
Rack1
Rackn
Rackn+1
Rackm
...
...
Login & Job Scheduler
HPC Application
Parallel
MPI-IO
Serial
POSIX
Parallel File System Client
I/O Libraries
OceanStor 100D File
Front-end network
Back-end network
SSD Pool
HDD Pool
Parallel high-performance client
Compatible with POSIX and MPI-IO: Meets the requirements of the high-performance compute application ecosystem and provides the MPI optimization library to contribute to the parallel compute community.
Parallel I/O for high performance: 10+ Gbit/s for a single client and 4+ Gbit/s for a single thread
Intelligent prefetch and local cache: Supports cross-file prefetch and local cache, and meets high-performance requirements of NDP.
Large-scale networking: Meets the requirements of over 10,000 compute nodes.
Collaborative scheduling of storage and compute resources
Huawei scheduler: service scheduling and data storage collaboration, data pre-loading to SSDs, and local cache
QoS load awareness: I/O monitoring and load distribution avoid scheduling based on compute capabilities and improve overall compute efficiency.
High-density customized hardware
All-flash Atlantic architecture: 5 U, 8 controllers, 80 disks, 70 Gbit/s IOPS per enclosure @ 1.6 million IOPS
High-density Pacific architecture: 5 U 120 disks, supporting online maintenance and providing a high ratio EC to ensure high disk rate.
Back-end network free: With the built-in switch module, the back-end network does not need to be deployed independently if the number of enclosures is less than 3.
Data tiering for cost reduction
Single view and multiple media pools: Ensure that the service view will not be changed and applications will not be affected by the change.
Traditional burst buffer free: The all-flash optimized file system simplifies the deployment of a single namespace and provides higher performance especially for metadata access.
NAS HPC Solution: Parallel High Performance, Storage and Compute Collaborative Scheduling, High-Density Hardware, and Data Tiering

## Slide 63
HDFS Service Solution: Native Semantics, Separation of Storage and Compute, Centralized Data Deployment, and On-Demand Expansion
Hadoop cluster
Management node
HDFS component
HDFS applications
Hadoop compute cluster
HDFS component
Distributed storage cluster
HDFS applications
......
Management node
......
Compute nodes
Compute nodes
Compute nodes
......
CPU
Memory
CPU
Memory
CPU
Memory
CPU
Memory
Compute node
Compute/Storage node
CPU
Memory
Storage system
Compute/Storage node
CPU
Memory
Storage system
Compute/Storage node
CPU
Memory
Storage system
Native HDFS semantics
Based on the general x86 server and Hadoop software, a compute/storage node is used to access the local HDFS. The compute and storage resources can be expanded concurrently.
OceanStor 100D HDFS is used to replace the local HDFS of Hadoop. Using native semantics for interconnection, storage and compute resources are decoupled. Capacity expansion can be performed independently, facilitating on-demand expansion of compute and storage resources.

## Slide 64
Incremental EC aggregates small objects into large objects without performance loss.
Reduce storage space fragments in massive small file storage scenarios, such as government big data storage, carrier log retention, and bill/medical image archiving.
Improve the space utilization of small objects from 33% (three copies) to over 80% (12+3).
SSD cache is used for object aggregation, improving the performance of a single node by six times (PUT 3000 TPS per node).
When the storage file object is smaller than the system strip, a large number of space fragments are generated, which greatly affects the space usage and access efficiency.
Node 1
...
Node 2
...
SSD Cache
SSD Cache
......
...
Obj1
Obj2
Obj3
Obj4
Obj5
Obj6
Strip1
Strip2
Strip3
Strip4
Object data aggregation
Performs incremental EC after small objects are aggregated into large objects
Parity 1
Parity 2
512K
EC 4+2 is used as an example.
Object Service Solution: Online Aggregation of Massive Small Objects Improves Performance and Capacity

## Slide 65
Unstructured Data Convergence Implements Multi-Service Interworking
O&M Management
Scenario: gene sequencing/oil survey/EDA/satellite remote sensing/IoV
Scenario: log retention/operation analysis/offline analysis/real-time search
Converged resource pool
Unstructured data base
Storage and compute collaboration
Out of the box
Intelligent O&M
Ecosystem compatibility
NAS
HDFS
Feature
Private client
Quota
Snapshot
Tiered storage
Asynchronous replication
Feature
Private client
Quota
Snapshot
Tiered storage
Rich ecosystem components
Multi-protocol interoperation
Variable-length deduplication and compression
Scenario: backup and archival/resource pool/PACS/check image
S3
Feature
Metadata retrieval
Quota
3AZ
Tiered storage
Asynchronous replication
Dedicated hardware
Competitive hardware differentiation
Integrated software and hardware, non-volatile memory, Huawei-developed SSD and NIC, and customized distributed storage hardware increase differentiated competitiveness.
High reliability
Dedicated hardware, fast sub-health isolation, and fast failover
Low cost
Ultra-high capacity density: HDD nodes provide 24 disks per U.
High performance
High-density performance: All-flash nodes provide 20 Gbit/s per U.
Converged storage pool
Three types of storage services share the same storage pool, reducing initial deployment costs.
Multi-protocol interoperation
Multiple access interfaces for one copy of data, eliminating the requirement for data flow and reducing TCO
Shared dedicated hardware
One set of dedicated hardware can be used for flexible deployment of three types of storage services, compatible with hardware components of different generations, implementing ever-new data storage.
Co-O&M management
One management interface integrates multiple storage services, achieving unified cluster and O&M management.
FILE
HDFS
OBJECT
Notes: Unstructured Data Convergence
Multiple servicers using FILE, HDFS and OBJECT storage can be located in the same storage pool, reducing initial deployment costs.
They use different interfaces for one copy of data, eliminating the requirement for data flow and reducing TCO.
Those services use one set of shared dedicated hardware for flexible deployment.
They use one management interface for unified management.
1) Converged storage pool
Three types of storage services share the same storage pool, reducing initial deployment costs.
2) Multi-protocol interoperation
Multiple access interfaces for one copy of data, eliminating the requirement for data flow and reducing TCO
3) Shared dedicated hardware
One set of dedicated hardware can be used for flexible deployment of three types of storage services, compatible with hardware components of different generations, implementing ever-new data storage.
4) Co-O&M management
One management interface integrates multiple storage services, achieving unified cluster and O&M management.