## Slide 1: NVMe, SCM etc
Chun Liu
Chun.Liu@Futurewei.com

## Slide 2: SAS NVMe SCM
NVMe vs SAS
  No more HBA, connect directly to PCIe
  More bandwidth, lower latency
SCM DIMM vs NVMe
  No more PCIe, connect directly to DRAM bus
  More bandwidth, lower latency
Latency
  Interface (DRAM < NVMe < SAS)
  Media (SCM < FLASH)
CPU
DRAM
SCM
DDR4 6 Channels
150GB/s, ~1200Gbps
PCIe Root
SAS HBA
PCIe Gen4 40 Lanes
640Gbps
PCIe X16
32Gbps
NVMe X4 8Gbps
x40
SCM
Optane DIMM
Optane Drive
SAS3 12Gbps

## Slide 3: Deeper Dive
Credit: SNIA NVMe Express: Optimizing for PCIe SSD Performance
FAST 2019: An Empirical Guide to the Behavior and Use of Scalable Persistent Memory
Notes: https://www.usenix.org/conference/fast20/presentation/yang

## Slide 4: NVMe-over-Fabric
Choice of Fabric: FC / Ethernet
  Ethernet: Huawei’s solution
  FC: Huawei’s solution
Credit: SNIA SDC 2016 Under the Hood with NVMe over Fabrics

## Slide 5: Use Cases
Cassandra
VMWare on NVMe
MySQL on NVMe
  Performance 3.5x improvement on NVMe SSD over SATA SSD
Credit: Percona live 17 Performance Analysis of NVMe SSDs and their Implication on Real World Databases
Notes: https://www.percona.com/live/17/sessions/performance-analysis-nvme-ssds-and-their-implication-real-world-databases

## Slide 6: SCM in Huawei’s Offering
Huawei 2280 server with Intel Xeno v6 and Intel optane DIMM
Huawei RoCE NIC
Huawei RoCE Switch

## Slide 7: SCM Use Cases (Huawei Prototypes)
Use SCM as Big Memory:
Optane Memory Mode
IaaS cost scaling
Use the SCM as Big NV Memory
Optane App Direct Mode
Huawei ALL SCM Prototype Machine